## Slide 1: DCO Project
Project Name: Digital high-frequency source on a chip - digitally controlled oscillator
Project Number: 22-1-12723
Students: Alisa Gumerova I.D. 956711378, Maya Shami I.D. 209369347
Project Mentor: Prof. Eran Socher
Project Location: VLSI Lab, Tel Aviv University
Mentor’s Signature:
_______________

## Slide 2: Project Topic
DPLL project, focusing on a DCO
DCO
LC tank (inductor + capacitor bank - controlled by switches) + Amplifier
non-linear circuit
converts DC power into a periodic electrical waveform
harmonic oscillator
our goal: designing and building a DCO from scratch

## Slide 3: DCO Specifications
Characteristic | Description | Target
VDD | Nominal operating voltage | 0.8 V
ftop | Upper oscillation frequency | 10.5 GHz
fbottom | Bottom oscillation frequency | 9.5 GHz
mtrxn | Digital varactor capacitors | 256
dfmtrx | Digital varactor resolution | 1.1 MHz
Is | Operational current | < 3mA
pn_100K | Phase noise at 100 kHz offset | -77 dBc/Hz
pn_1M | Phase noise at 1 MHz offset | -100 dBc/Hz
pn_10M | Phase noise at 10 MHz offset | -120 dBc/Hz

## Slide 4: Our Workflow
Theoretical calculations based on the project specifications
Schematic-level design
Simulations
Layout
Extraction
Simulations and verification

## Slide 5: DPLL: Block Diagram

## Slide 6: DCO: Block Diagram
All blocks are implemented by us
Using Virtuoso
LC tank
  Inductor
  Capacitor bank: coarse
  & fine-tuning unit cell
  Capacitor matrix: very fine tunning
Differential amplifier

## Slide 7: Calculations
Inductor
Final inductor size is
  and
Capacitor bank & matrix
⇒ ,
⇒ size of capacitance range:
⇒ (fine tuning capacitor)
Frequency-band overlap:
⇒ 27 sub-bands
Large caps  large area, high parasitics
 solution: further division of the bank
(2 coarse caps (each), 8 fine caps ( each))
Capacitor matrix – logic:
En = ~col_off + col · row = ~ (col_off · (~ (col · row))
col[i] | row[j] | col_off[i] | En[i][j]
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 8: Simulations
Cross-coupled oscillator
Non-ideal components chosen from analoglib
Goal: lower oscillation frequency of 8.55 GHz , upper oscillation frequency of 11.235 GHz (10% below and 7% above the spec)
Result: 8.4 GHz, 11 GHz

## Slide 9: Inductor – Implementation
Final inductor size is
Layout of 1.2nH inductor
Schematic of the inductor for SP simulation

## Slide 10: Inductor – Simulation Results
S-parameter simulation and calculation of the inductance and the Q

## Slide 11: Capacitor Matrix – Single Cap
Built in Hierarchal manner: Single capacitor Single cell Single cell with logic 4-cells with logic The matrix (256 cells)
A single capacitor
Layout of capacitor.
Schematic of a single capacitor for SP simulation

## Slide 12: Capacitor Matrix – Single Cap
S-parameter simulation and extraction of the capacitor size and the Q

## Slide 13: Capacitor Matrix – Single Cell
Schematic of A single cell for the simulation of

## Slide 14: Capacitor Matrix – Single Cell:
Simulation’s results for Enable = 0 & Enable = 1.
To calculate the :

## Slide 15: Capacitor Matrix – Cell
A single cell with logic
The logic: En = ~col_off + col · row = ~ (col_off · (~ (col · row))
Schematic and Layout of a single cell with logic.

## Slide 16: Capacitor Matrix – 4 Cells
4-cells block - an intermediate step to ease the layout process of the whole matrix
Schematic and Layout of 4-cells block.

## Slide 17: Capacitor Matrix – Whole
The whole matrix
Schematic and Layout of the whole matrix

## Slide 18: Capacitor Matrix – Simulations & Results
OFF Mode: col<0:15> & Row<0:15> -VSS, Col_off<0:15> -VDD
ON Mode: col<0:15> & Row<0:15> -VDD, Col_off<0:15> VSS
Schematic of simulation for calculation
Results of ON and OFF modes of the matrix

## Slide 19: Capacitor Bank
2 sub-blocks: coarse (2 cells, 36fF each), fine (8 cells, 4fF each)
Both use differential switches
  Transistor (switch)
  2 biasing resistors (+ invertor)

## Slide 20: Capacitor Bank - Fine-Tuning: Cell
Goal: ΔC = 4fF + spare
Before extraction: ΔC = 5.03fF
After extraction: ΔC = 4.77fF

## Slide 21: Capacitor Bank - Fine-Tuning: Block
8 cells in parallel – connections through a high metal

## Slide 22: Capacitor Bank - Coarse-Tuning: Cell
Identical to fine-tuning, except:
  Larger capacitors
  Larger transistors – 2 in parallel to achieve a wider effective gate
Goal: ΔC = 36fF + spare
Before extraction: ΔC = 40.4fF
After extraction: ΔC = 38.27fF

## Slide 23: Capacitor Bank - Coarse-Tuning: Block
2 cells in parallel – connections through a high metal

## Slide 24: Capacitor Bank – Full Layout

## Slide 25: LC Tank

## Slide 26: LC Tank - Summary of Results

## Slide 27: Amplifier

## Slide 28: DCO

## Slide 29: Challenges and the Solutions

## Slide 30: Final simulations & results
 | Parameter | Target - spec | Simulation results
 | Is - Operational current | < 3mA | ON – 2.367 mA OFF – 2.194 mA
 | f_bot - Bottom oscillation frequency | 9.5 GHz (with spare 8.55GHz) | 8.98 GHz
 | f_top - Upper oscillation frequency | 10.5 GHz (with spare 11.235 GHz) | 12.34 GHz
 | mtrx_n - Digital varactor capacitors | 256 | 256
 | df_mtrx – Minimal jump in tuning range | < 1.2 MHz | 1.1 MHz
 | Pn_100K – Phase noise at 100kHz offset | -77 dBc/Hz | ON – -72.547 dBc/Hz OFF – -64.955 dBc/Hz
 | Pn_1M – Phase noise at 1 MHz offset | -100 dBc/Hz | ON – -100.130 dBc/Hz OFF – -93.412 dBc/Hz
 | Pn_10M – Phase noise at 10 MHz offset | -120 dBc/Hz | ON – -122.913 dBc/Hz OFF – -117.403 dBc/Hz

## Slide 31: Final simulations – Transient (ON state)

## Slide 32: Final simulations – Transient (OFF state)

## Slide 33: Final simulations – hbnoise (ON state)

## Slide 34: Final simulations – hbnoise (OFF state)

## Slide 35: Conclusions & Future work
Increasing the amplifier gain
Lowering area – more loops in the inductor, improving routing
Lowering frequency – adding a fixed cap

## Slide 36
Thank you for your attention!